## Slide 1
FLUID | COMPONENT | DESIGN CODE | MATERIAL |  |  | INSULATED (Y/N) | OP. PARAMETER |  | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Shell General Corrosion External ATMOSPHERIC CORROSION
 |  |  | TYPE | SPEC | GR |  | T (֯C) | P (Mpa) |  | 
1 | Rolled Shell Plate (1571x600x5mm) | - | Stainless Steel | SA 240 | 316L | - | 100 °C | 1.0 BarG | LOW | 
- | Dish Head (8 thk, TD 2:1) | - | Stainless Steel | SA 240 | 316L | - | 100 °C | 1.0 BarG |  | 
- | Seamless Pipe (DN50, 8.7 SCH 40s) | - | Stainless Steel | SA 312 | TP 316L | - | 100 °C | 1.0 BarG |  | 
- | Seamless Pipe (DN25, 100 SCH 40s) | - | Stainless Steel | SA 312 | TP 316L | - | 100 °C | 1.0 BarG |  | 
- | Seamless Pipe (DN150, 11.2 SCH 40s) | - | Stainless Steel | SA 312 | TP 316L | - | 100 °C | 1.0 BarG |  | 
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM (Correction Factor) | 100% of TML Location – Refer TML as per Attachment | General Corrosion
VISUAL INSPECTION | External Visual Inspection (100% Coverage) With follow up by UT, RT, or pit gauge as required. | Atmospheric Corrosion

## Slide 2
FLUID | COMPONENT | DESIGN CODE | MATERIAL |  |  | INSULATED (Y/N) | OP. PARAMETER |  | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Shell General Corrosion External ATMOSPHERIC CORROSION
 |  |  | TYPE | SPEC | GR |  | T (֯C) | P (Mpa) |  | 
- | Flange (DN50, Class 150 WNRF SCH 40s) | - | Stainless Steel | SA 182 | F316L | - | 100 °C | 1.0 BarG | LOW | 
- | Flange (DN25, Class 150 WNRF SCH 40s) | - | Stainless Steel | SA 182 | F316L | - | 100 °C | 1.0 BarG |  | 
- | Flange (DN150, Class 150 WNRF SCH 40s) | - | Stainless Steel | SA 182 | F316L | - | 100 °C | 1.0 BarG |  | 
- | Base Plate (150x150x5 thk) | - | Stainless Steel | SA 240 | Gr. 304 | - | 100 °C | 1.0 BarG |  | 
- | Lifting Lug Plate (190x80x6 thk) | - | Stainless Steel | SA 240 | Gr. 304 | - | 100 °C | 1.0 BarG |  | 
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM (Correction Factor) | 100% of TML Location – Refer TML as per Attachment | General Corrosion
VISUAL INSPECTION | External Visual Inspection (100% Coverage) With follow up by UT, RT, or pit gauge as required. | Atmospheric Corrosion

## Slide 3
FLUID | COMPONENT | DESIGN CODE | MATERIAL |  |  | INSULATED (Y/N) | OP. PARAMETER |  | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Shell General Corrosion External ATMOSPHERIC CORROSION
 |  |  | TYPE | SPEC | GR |  | T (֯C) | P (Mpa) |  | 
- | Doubler Plate (120x150x12.7 thk) | - | Stainless Steel | SA 240 | Gr. 304 | - | 100 °C | 1.0 BarG | LOW | 
- | Equal Angle Bar (3"x3"x1/4" thk) | - | Stainless Steel | SA 240 | Gr. 304 | - | 100 °C | 1.0 BarG |  | 
- | Earthing Lug | - | Stainless Steel | SA 240 | Gr. 304 | - | 100 °C | 1.0 BarG |  | 
- | - | - | - | - | - | - | - | - | - | -
- | - | - | - | - | - | - | - | - | - | -
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM (Correction Factor) | 100% of TML Location – Refer TML as per Attachment | General Corrosion
VISUAL INSPECTION | External Visual Inspection (100% Coverage) With follow up by UT, RT, or pit gauge as required. | Atmospheric Corrosion