## Slide 1
FLUID | COMPONENT | DESIGN CODE | MATERIAL |  |  | INSULATED (Y/N) | OP. PARAMETER |  | CURRENT RISK RATING | Corrosion Group : Damage Mechanism Susceptible: Internal Shell General Corrosion External ATMOSPHERIC CORROSION
 |  |  | TYPE | SPEC | GR |  | T (֯C) | P (Mpa) |  | 
HOT WATER | SHELL PLATE | - | Stainless Steel | ASTM A240 | 304L | - | 90 C | 1 BarG | LOW | 
HOT WATER | ELLIPSOIDAL HEAD | - | Stainless Steel | ASTM A240 | 304L | - | 90 C | 1 BarG |  | 
HOT WATER | FLANGE | - | Stainless Steel | ASTM A182 | F304L | - | 90 C | 1 BarG |  | 
HOT WATER | NECK | - | Stainless Steel | ASTM A312 | TP304L | - | 90 C | 1 BarG |  | 
HOT WATER | NECK | - | Stainless Steel | ASTM A240 | 304L | - | 90 C | 1 BarG |  | 
INSPECTION METHOD | INSPECTION COVERAGE | DAMAGE MECHANISM
UTTM (Correction Factor) | 100% of TML Location – Refer TML as per Attachment | General Corrosion
VISUAL INSPECTION | External Visual Inspection (100% Coverage) With follow up by UT, RT, or pit gauge as required. | Atmospheric Corrosion
Expansion Tank
V-001
MLK_PMT_10104_-_V-004